Task summary: You are tasked to design a minimum length 2-dimensional rocket engine nozzle for the specific conditions given below. The analytical procedure called, Method of Characteristics, as described in Section 11.7, p. 397, and Example 11.1, p. 401 of your textbook, may be used to tackle this project.

Your design must be presented in a report form by each student, with the description of design procedure, sample calculations, plots and table of calculated results and any program listing that you developed. A scaled drawing of the nozzle must also be given. You are expected to use either Fortran, C++, or Matlab programming to develop the nozzle contour.

DUE DATE: 5:00 pm, April 28, 2010. Late submissions will not be graded. All plagiarized reports will receive a zero credit and possible failure in the course.

General Specifications:
1. The rocket is to discharge into an atmosphere where the ambient pressure is 101 kPa. Note that for this ambient pressure the nozzle flow is expected to be over-expanded and a shock wave occurs at the exit. Find out for what exit pressure the nozzle will be completely shock free.
2. The propellant is a mixture of hydrogen and oxygen, with  = 1.22 and R = 519.6 J/(kg.K)
3. The stagnation temperature T0 of the propellant is 3000 K, and the stagnation pressure p0 of the propellant is 1700 kPa
4. The total mass flow rate, size 12{ {m} cSup { size 8{ "." } } } {} , through the rocket nozzle is 0.2 kg/s
5. The velocity of the fluid as it crosses the exit plane must be uniform and parallel to the axis of symmetry
6. The overall expansion ratio Aexit/Athroat must be large enough so that the specific kinetic energy of the exhaust gas, 0.5 Ve2 is as high as possible percentage of the specific stagnation enthalpy, h0, of the propellant. What is the best percentage of this kinetic energy of exhaust with respect to the specific stagnation enthalpy, h0, of the propellant?
7. The geometry should not exhibit sharp corners of large turning angles (this is required to avoid boundary layer separation due to sharp corners)
8. The length of the nozzle should be as short as possible subject to above constraints

Design solution presentation: Your report must include (among other things) the following information;
  1. A table of the nozzle interior contour coordinates. The coordinates must be expressed in SI units, as measured from the axis of symmetry as a function of axial distance, x, from the throat section.
  2. You must also include explicit calculations of the exit speed, Ve, and the exit Mach number, Me.
  3. Use suitable number of characteristics to produce a smooth contour.
  4. Program listing must be presented, if one is used.
  5. Provide a smoothed graphics of your final nozzle shape.
  6. Provide a discussion of nozzle flow characteristics.

Useful References:
Liepmann, H. W. and Roshko, A., Elements of Gas Dynamics, John Wiley and Sons. Inc., 1957
Zucrow, M. J. and Hoffmann, J. D., Gas Dynamics, Krieger Publishing Company, 1985
Shapiro, A. H., The Dynamics and Thermodynamics of Compressible Flows, Vol.1, The Ronald Press Co., N.Y., 1953